FEATURES

* Frequency Range: 0.3Hz ~ 3MHz    (GFG-8215A/8216A/8217A/8219A)

* Frequency Range: 0.5Hz ~ 5MHz (GFG-8250A/8255A)

* Waveforms: Sine, Triangle, Square,, Ramp,    TTL and CMOS Output

* External Voltage Controlled Frequency (VCF) Function

* Duty Cycle Control with Signal Inversion Capability

* Variable DC Offset Control

* Two-Step (-20dBx2) and Variable attenuator

* Built-in 6 Digit Counter with INT/EXT

Function up to 150MHz (Except GFG-8215A)

* LIN/LOG Sweep Mode   (GFG-8217A/8219A/8255A)

* INT/EXT 	AM/FM Modulation (GFG-8219A/8255A)

* GCV Output for Synchronization (GFG-8219A/8255A)

The GFG-8200A product family offers a complete solution in generating signals at the frequency ranges of 3&5 MHz. All models are embedded with standard functions such as TTL/CMOS/Ramp output, External Voltage Controlled Frequency (VCF), as well as built-in 6-digit counter (except for GFG-8215A).  Further versatility of Logarithmic and Linear sweep is added into GFG-8255A/8219A/8217A, while GCV output feature and AM/FM modulation are available in GFG-8255A/8219A.. All these integrated functions and user-friendly operations of the GFG-8200A series are made to accommodate the applications in audio response testing, vibration testing, servo system evaluation, ultra sound applications, etc.

GFG-8217A (3MHz)

MODEL DISPLAY WAVEFORM

FREQUENCY RANGE LIN/LOG SWEEP AM/FM MODULATION FREQUENCY COUNTER VOLTAGE CONTROL

FREQUENCY

GCV OUTPUT TTL/CMOS OUTPUT

Made to Measure.

Good Will Instrument Co., Ltd.

# Text boxes

| MODEL SPECIFICATION | GFG-8215A/8216A/8217A/8219A S | GFG-8250A / 8255A |
| --- | --- | --- |
| MAIN |  |  |
| Frequency Range Amplitude Impedance Attenuator DC Offset Duty Control Display Range Accuracy | 0.3Hz ~ 3MHz (7 Range) > 10Vpp (into 50W load) -20dB 1dBx2 <-5V ~ >5V (into 50W load) 80% : 20% : 80% to 1MHz Continue variable 6 digit LED display *GFG-8215A does not have display. 50W 10%+_ +_ +_ 5%+1Hz (at 3 position) *only for GFG-8215A | 0.5Hz ~5MHz (7 Range) > 10Vpp (into 50W load) -20dB 1dBx2 <-5V ~ >5V (into 50W load) 80% : 20% : 80% to 1MHz Continue variable 6 digit LED display 50W 10%+_ +_ |
| SINE WAVE |  |  |
| Flatness Distortion | (Specification applied from MAX. to 1/10 level) 1%, 0.3Hz ~ 200kHz THD 35dB below < 0.3dB, 0.3Hz ~ 300kHz < 0.5dB, 300kHz ~ 3MHz fundamental in all range <_ <_ | 1%, 0.5Hz ~ 100kHz THD 30dB below (Specification applied from MAX. to 1/10 level) 0.3dB, below 500kHz 1dB, below 5MHz fundamental in all range <_ <_ <_ <_ |
| TRIANGLE WAVE |  |  |
| Linear | 98%, 0.3Hz ~ 100kHz>_ | 98%, 0.5Hz ~ 100kHz>_ |
|  | 95%, 100kHz ~ 3MHz>_ | 95%, 100kHz ~ 5MHz>_ |
| SQUARE WAVE |  |  |
| Rise or Fall Time Symmetry | +_ 100nS at maximum output (into 50W load) 2%, 0.3Hz ~ 100kHz <_ | +_ 50nS at maximum output (into 50W load) 2%, 1Hz ~ 100kHz <_ |
| CMOS OUTPUT |  |  |
| Rise or Fall Time Level | +_ +_ 120nS 4Vpp 1Vpp ~ 14.5Vpp 0.5Vpp adjustable <_ | +_ +_ 120nS 4Vpp 1Vpp ~ 14.5Vpp 0.5Vpp adjustable <_ |
| TTL OUTPUT |  |  |
| Level | 3Vpp>_ | 3Vpp>_ |
| Fan Out | 20 TTL load | 20 TTL load |
| Rise or Fall Time | 25nS<_ | 25nS<_ |
| VCF (Voltage Cont | rolled Frequency) |  |
| Input Impedance Input Voltage | +_ +_10kW 10% 0V ~ 10V 1V (100 : 1) | +_ +_10kW 10% 0V ~ 10V 1V (100 : 1) |
| GCV (Generator Co | ntrolled Voltage) (GFG-8219A/8255A) |  |
| Output Voltage | To set the voltage between 0V ~ 2V as | To set the voltage between 0V ~ 2V |
|  | per different frequency | as per different frequency |
| SWEEP OPERATI | ON (GFG-8217A/8219A/8255A) |  |
| Sweep/Manual | Switch selector | Switch selector |
| Sweep/Rate | 100 : 1 ratio max. and adjustable | 100 : 1 ratio max. and adjustable |
| Sweep/Time | 0.5sec. ~ 30sec. adjustable | 0.5sec. ~ 30sec. adjustable |
| Sweep/Mode | Lin./Log. switch selector | Lin./Log. switch selector |
| AMPLITUDE MO | DULATION (GFG-8219A/8255A) |  |
| Depth MOD. Frequency Carrier BW EXT Sensitivity | 0 ~ 100% 400Hz (INT), DC ~ 1MHz(EXT.) 100Hz ~ 3MHz (-3dB) 10Vpp for 100% modulation<_ | 0 ~ 100% 400Hz (INT), DC ~ 1MHz(EXT.) 100Hz ~ 5MHz (-3dB) 10Vpp for 100% modulation<_ |

| GFG-8255A | GFG-8250A | GFG-8219A | GFG-8217A | GFG-8216A | GFG-8215A |
| --- | --- | --- | --- | --- | --- |
|  | 6 Digits LED Display |  | - |
|  | Sing , Square , Triangle |  |  |
| 5MHz | 5MHz | 3MHz | 3MHz | 3MHz | 3MHz |